## Slide 1
DIY Secret Code Lock Circuit
Using XOR and NOR Gates
A4-bit digitalsecretcodelock circuit implementedwithCMOSICs 4070
(XOR) and4001(NOR),powered bya 9 VDCsupply.

## Slide 2
Circuit Overview
Power
Inputs
Outputs
Logic ICs
9VDCsupply for reliable operation.
8digitalinputs: S1-S4 (Set Code), E1-E4 (Enter Code).
GreenLED (Unlock), Red LED (Lock), Electric lock via TIP122
Darlington transistor.
IC4070forXOR comparison, IC 4001 for NOR logic. No AND gates
used.

## Slide 3
Project Objectives & Key Components
Objective
Key Components
Designa4-bitcombinational digital lock using CMOS logic.
S1-S4 (preset), E1-E4 (user input).
TIP122 Darlington transistor for electric lock.
Bit-by-bit comparison, LOW output if bits match.
Combines XOR outputs, HIGH only if all XOR outputs are LOW.
02
03
04
01
Code Setting & Entry
Output Driver
NOR Decision (IC 4001)
XOR Comparison (IC 4070)

## Slide 4
Advantages & Future Scope
Advantages
Future Enhancements
Simple & Reliable
Low Power CMOS
No Microcontroller
Expand CodeBits
Keypad Interface
Electronic Inputs
Efficient operation at 9 V.
Pure logic gate implementation.
Straightforwarddesign,robust operation.
Integrateakeypadforcode entry.
Replacemechanicalswitches with advanced
electronic inputs.
Increasesecuritybyadding more code bits.